## Slide 1: The dynamic host configuration protocol

## Slide 2: What is the DHCP?
Organizes dynamic distribution of network configuration parameters
Responsible for a (limited) pool of IP Addresses
DHCP Server Fixed IP - 000
IP1 - 111 IP2 - 222 IP3 - 333
Smartphone
IP 111
New Tv
IP ?
Computer
IP 333
IP Request (UDP Based)
Notes: Check -> At home, ‘dhcp’ is a part of your router? Your router gets 1 fixed IP address from proximus/telenet, and has several dynamic IP addresses behind it for your homenetwork? Which makes it harder to set up a private server (since servers need fixed IP’s) ? Is this what ‘a switch’ is?

## Slide 3: Allocation of IP Addresses
Dynamic Allocation
  Lease with controllable time
Automatic Allocation
  Keep track of previous IP addresses and try to reassign the same address
Manual Allocation
  MAC binding of IP
  If not possible: Server may fall back on dynamic/automatic allocation

## Slide 4: Characteristics
Policies can be fixed
  Fixed leasing time
  Change IP after fixed time
  Reserve some IP’s for specific users
Efficient: IP reusable when device leaves network
  1000 users, maximum 200 at same time? Only 200 IP’s needed.
Notes: - When a device requests a new IP Address during the leasetime of its current IP, the server first tries to reassign the current IP Address to the same device again (so usually, you keep using the same IP)

## Slide 5: How it works: The DORA Process
DHCP Discovery
DHCP Offer
DHCP Request
DHCP Acknowledgement
Notes: DISCOVERY: New device does broadcast -> Received by all devices and servers in the network
OFFER: Only the DHCP server(s) respond to the request -> It/they send(s) a free IP addresss to te MAC address of the new device
REQUEST: New device knows which IP Address is/are accessible and requests to use the IP of the server who first responded
ACKNOWLEDGEMENT: Server accepts the request. Device should now double check IP to make sure no other device has this IP
! Security issues here: fake DHCP servers can provide invalid info to clients / fake clients can keep on sending dummy requests to servers in order to exhaust them. Validation checks are not always built in

## Slide 6: DORA the explorer

## Slide 7: Upscaling: The DHCP Relay Agent
Main DHCP Server | 
First subnet of computers | 111 – 123 111 – 456
Second subnet of computers | 222 – 123 222 – 456
Relay Agent First subnet
IP 111
Relay Agent Second subnet
IP 222
Device1
111 - 123
Device1
222 -123
Device2
111 - 456
New Device2
?
New Request
New 222 request
Notes: Onder voorbehoud – Dubbelchecken bij Thomas of Seppe ;)

## Slide 8: DHCP VS static IP
“Plug and play”
No manual configuration
# IP addresses = size of pool

## Slide 9: DHCP VS static IP
Manual assign IP address
You need to:
  enter the IP address
  the subnet mask
  the default gateway
  the DNS server(s).

## Slide 10: Dangers of DHCP
Less control  everyone can connect to your network
Unauthorized DHCP server under someone else control
   For most home networks, DHCP is fine
Static IP:
  More work, but
  You control to whom you give an IP address

## Slide 11: DHCP VS Static IP
DHCP | Static IP
Request IP automatically | Manual configuration of IP
Central configuration | Set for each new device
Device in other subnet? No manual changes needed | Each change has to be set for each device
IP can change | A device contains a fixed IP