## Slide 1
IP addresses

## Slide 2: Example
You are on vacation and you want to send a postcard to your parents
  What do you do to make sure the card arrives?
  What are the different parts of an address?
    Street
    Number
    Zip code
    City
    (Country)

## Slide 3: How does this work in a computer network?
In a computer network each computer sends messages to other computers
How do they make sure that the message arrives on the right computer?
  Computers also have an address
    MAC-address (unique identification of your network interface card)
      Used for communication inside the same subnet
    IP-address
      Used for identification of computers on different subnets/networks
Notes: MAC stands for Media Access Control, are most often assigned by the manufacturer and stored in its hardware
IP stands for Internet Protocol

## Slide 4: What is an IP-address
Sequence of ones and zeroes (32 bits for IPv4)
  11000000101010000000000000000001
This notation is not readable for humans, so we can convert this to a decimal notation
  Split it up in 4 octets (bytes)
    11000000.10101000.00000000.00000001
  Convert each byte to its decimal notation
    Value between 0 and 255
Decimal notation: 192.168.0.1

## Slide 5: Different parts of an IP-address
Network identification
  This identifies the network of your computer
Host identification
  This identifies the computer inside the network

## Slide 6: Discover the network identification in you IP-address
Example: What is the network address of 10.165.32.5?
  What do you need to filter the network address from your IP?
    Subnet mask: 255.255.0.0
  How do you do this filtering?
    Convert the decimal notation to binary notation
    Calculate the network address using a logical AND
      00001010.10100101.00010000.000000101
      11111111.11111111.00000000.000000000
      00001010.10100101.00000000.000000000
    Convert back to decimal notation
      10.165.0.0

## Slide 7: What is a valid subnet mask?
Is 255.16.0.0 valid?
  NO!
Subnet mask is a sequence of ones followed by a sequence of zeroes
  The ones identify the network address
  The zeroes identify the host address
Possible notation
  Dotted notation 192.168.0.1 subnet mask 255.255.0.0
  Prefix notation 192.168.0.1/16

## Slide 8: Different classes in IP-addresses (ClassFull)

## Slide 9: Private ranges in IP addresses
Addresses that are not routable on the internet
Result: These addresses can be reused in different networks
Has anyone ever tried to look at his/her/its IP-address at home?
  Mostly it’s something like 192.168.0.x
  This applies for the most of us, maybe not for Roel… 
Class A: range: 10.0.0.0 – 10.255.255.255
Class B: range: 172.16.0.0 – 172.31.255.255
Class C: range: 192.168.0.0 – 192.168.255.255
How can multiple hosts have the same IP address?
  Ask the group that will present NAT!

## Slide 10: Special addresses
Linklocal loopback address: 127.0.0.1
  The same as typing localhost in your browser
    Localhost:8080 == 127.0.0.1:8080
Broadcast address
  IP-address with all ones in the host address
  Used to send broadcast messages on a network
  192.168.255.255

## Slide 11: IP Address exhaustion
IP addresses are limited
If a company has too many hosts to fit inside of a class C address, they get a class B address. Probably they don’t have this many hosts
  A lot of IP addresses are/were wasted
Solution: ClassLess
  No fixed size classes
  If a company only needs 7 hosts, they will only get 7 addresses
    This is where subnet masks like 255.255.255.128 come in
    More possible networks with the same amount of IP addresses

## Slide 12: IPv6
Still the number of IP addresses is very limited in our digital world
With the rise of smartphones and IoT (or even IoE) we need a lot more IP addresses
IPv6 is a new notation with a bigger range
  128 bits, so a lot of ones and zeroes!
  Notation: divided in 8 groups of 4 hexadecimal digits (0-F)
    16 bits per group
    1234:5678:9ABC:DEF0:1234:5678:9ABC:DEF0
  Fixed length network and host part: 64 bits each (4 groups)
  Can also be subnetted

## Slide 13: Subnets?
You can divide your network into different smaller sub networks
Why?
  Security
  Separating logical groups of hosts
    Computers
    Printers
    Servers
    …
How?
  Broaden the network address and change your subnet masks
  You can calculate this, but we’ll leave this out of scope
    https://www.pluralsight.com/blog/it-ops/simplify-routing-how-to-organize-your-network-into-smaller-subnets